Paul Huddlestun

Logged - 3/73

Redrawn – 9/25/09

Written up – 11/12/11

GEORGIA POWER, B37 (POOR ROBIN LANDING)

SCREVEN COUNTY, GEORGIA

Blue Springs Landing 7½’ Quadrangle

On the side of an unimproved, east-west dirt road,

approximately 0.3 mile south of the jct. of Poor Robin Road and Heather Lane,

0.15 mile west of what appears to be a small Carolina Bay,

About 1.1 miles west of the site of core B36, above river floodplain,

in eastern Screven County, GA

Latitude		32° 42.291’                      Elevation ~100 Feet

Longitude		81° 25.564’

Lithostratigraphic

unit and bed number       Description                                 Thickness      Depth

__(feet)_  (feet)

NO CORE                                                                                 65.0              0.0

DISCONTINUOUS CORING – CORE SAMPLES CONSIST OF 1.5 FEET OF  CORING FOR EVERY 5 FEET OF DRILLING; DISCONTINUOUS CORING CONTINUED FROM 65.0 FEET TO THE TOP OF THE SUWANNEE LIMESTONE ROUGHLY AT 120.0 FEET.  LITHOLOGIES AND STRATIGRAPHIC UNITS APPROXIMATED:

UPPER PLIOCENE, PIACENZIAN

CYPRESSHEAD/ALTAMAHA FORMATION?/SCREVEN MEMBER? – 15 feet(

Bed 1		Sand: medium to coarse grained and                       11.5             65.0

moderately to poorly sorted with some

granules in the lower part, slightly

argillaceous in the upper part but clay is

not apparent in the lower part; massive and

structureless; unconsolidated; overlies core

gap:

CORE GAP                                                                                    3.5             76.5 LOWER MIOCENE, AQUITANIAN
PARACHUCLA FORMATION

Tiger Leap Member – 40 feet

Bed 2		Sand: coarse to very coarse grained; slightly            1.5             80.0

argillaceous and very slightly phosphatic

with pelletal phosphate; massive and

structureless; unconsolidated; overlies core

gap:

CORE GAP                                                                                    3.5             81.5

Bed 3		Sandy clay/clayey sand: quartz sand is poorly          6.5             85.0

sorted; phosphatic; massive and structureless;

unconsolidated; overlies core gap:

CORE GAP                                                                                    3.5             91.5

Bed 4		Clay: slightly pelletal phosphatic, fine to                 6.5             95.0

medium grained sand on partings in the

lower part, gypsum bloom on the surface of

the core; thinly layered to laminated;

unconsolidated; overlies core gap;

CORE GAP                                                                                   3.5            101.5

Bed 5		Sand: coarse grained; phosphatic, probably             1.5            105.0

a trace of clay minerals; massive and

structureless; unconsolidated, incoherent

and loose; overlies core gap:

CORE GAP                                                                                  3.5            106.5

Bed 6		Sand: calcareous, slightly argillaceous and              1.5            110.0

phosphatic, fossiliferous; massive and

structureless; unconsolidated; overlies core

gap:

CORE GAP                                                                                   3.5            111.5

Bed 7		Clay: slightly calcareous and phosphatic                  1.5            115.0

with small shell debris along partings, no

apparent sand; thinly layered to laminated;

unconsolidated and tough; overlies core gap:

CORE GAP                                                                                  3.5            116.5

LOWER OLIGOCENE, VICKSBURGIAN

SUWANNEE LIMESTONE – 20.7 feet

Bed 8		Limestone: very deeply weathered, some                  1.5            120.0

discernible clay and fossils; overlies “cavity”:

CAVITY                                                                                      19.2            121.5

UPPER EOCENE, UPPER JACKSONIAN

OCALA GROUP

BRYOZOAN LIMESTONE – 72.3 feet

Crystal River-equivalent

Bed 9		Limestone: bryozoan-rich; massive and                    7.3            140.7

structureless; hard, tough and indurated;

grades downward into:

Bed 10	Limestone: bryozoan-rich, massive and                  15.0            148.0			structureless; hard, tough and indurated

but poor recovery; probably overlies core

gap of undetermined extent:

Bed 11	Limestone: subcoquinoid, bryozoan-rich,                10.0            163.0

relatively loosely packed; massive and

structureless partially indurated;  grades

downward into:

Bed 12	Limestone: bryozoan-rich with soft, chalky,              3.0            173.0

fine textured matrix. massive and

structureless; poorly consolidated; grades

downward into:

Bed 13	Limestone: subcoquinoid and bryozoan-rich;            7.0            176.0

massive and structureless; indurated, hard

and brittle; “white” in color; abruptly overlies:

Bed 14	Limestone: coquinoid, medium to coarse                15.0            183.0

textured; bioclastic texture fines downward;

massive and structureless; indurated	; grades

downward into:

Parachucla-equivalent – 15 feet

Bed 15	Limestone: sandy and fossiliferous; echinoids        10.0            198.0

at ~203 feet; massive and structureless;

grades downward into:

Bed 16	Limestone: sandy, nonfossiliferous; massive            5.0            208.0

and structureless; grades downward into:

UPPER EOCENE, LOWER JACKSONIAN

BARNWELL GROUP

DRY BRANCH FORMATION

Griffins Landing Member  –  20 feet(

Bed 17	Very calcareous sandstone/very sandy                  20.0            213.0

limestone: abundant molds of mollusks,

probably a trace of clay minerals, no other

lithic components noted; massive and

structureless; consolidated, hard and

friable; bottom of the core at 233 feet.

____________________________                                                                                  TOTAL DEPTH – 233.0 FEET

Core was disposed of in 1973/1974