Paul Huddlestun

Logged ca. 1973

Redrawn – 3/84

Written up – 6/6/14

HOUSTON 4 (CLINCHFIELD/MEDUSA LIME PIT), GGS-3058

HOUSTON COUNTY, GEORGIA

Approximately 0.75 mile southeast of jct. Keys Road and US 341

at Clinchfield, Houston County, Georgia, at the site of the Medusa lime pit,

on the south side of Highway US 341

Latitude		N 32° 24.100’                           Elev. 382 Feet

Longitude		W 83° 37.988’

Lithostratigraphic

unit and bed number         Description                           Thickness          Depth  _________________________________________________________(feet)__________(feet)_

NO CORE                                                                               45.0              0.0

UPPER EOCENE, LOWER JACKSONIAN

BARNWELL GROUP

DRY BRANCH FORMATION

Twiggs Clay Member – 95 feet±

Bed 1	Sand: fine to medium grained and moderately        5.0             45.0

well sorted; slightly argillaceous, calcareous

and fossiliferous; massive and structureless;

overlies core gap:      ~

NO CORE                                                                                45.0             50.0

UPPER EOCENE, LOWER JACKSONIAN

TIVOLA LIMESTONE – 34 feet+

Bed 2		Limestone: bioclastic and calcarenitic;                    2.5             95.0

argillaceous and fossiliferous; soft but

consolidated; overlies:

Bed 3		Limestone: fine textured matrix with coarser,         4.5             97.5

bioclastic debris; massive and structureless;

crystalline and dense; overlies:

Bed 4		Limestone:  medium to coarse textured,                4.0            102.0

bioclastic and subcoquinoid; massive and

structureless; overlies:

Bed 5		Limestone: medium textured, calcarenitic              9.5            106.0

and fossiliferous with abundant bryozoans;

massive and structureless; fairly loose and

poorly consolidated; overlies core gap:

CORE GAP                                                                               2.5            115.5

Bed 6		Limestone: fine to medium textured and                1.0            118.0

chalky, no macrofossils noted; structureless;

soft and apparently poorly coherent; overlies:

Bed 7		Limestone: porous and subcoquinoid with           10.0            119.0

abundant Lepidocyclina; massive and

structureless; soft but somewhat consolidated

and brittle; overlies:

UPPER/MIDDLE EOCENE? LOWER JACKSONIAN?/UPPER CLAIBORNIAN?

BARNWELL GROUP

CLINCHFIELD SAND – 6 feet

Bed 8		Sandstone: very calcareous and fossiliferous;        1.0            129.0

apparently structureless; hard and indurated;

overlies:

Bed 9		Sandstone: medium to coarse grained and            4.0            130.0

moderately well sorted; very calcareous with

scattered fossil molds; massive and

structureless; indurated; overlies;

Bed 10	Sandstone: fine to medium grained and                 1.0            134.0

moderately well sorted; calcareous;

structureless; very abruptly and

disconformably overlies:

MIDDLE EOCENE, UPPER CLAIBORNIAN

LISBON FORMATION

Blue Bluff Member – 37.0 feet

Bed 11	Clay: finely sandy, calcareous and glauconitic       8.0            135.0

with scattered shells and shell fragments;

massive and structureless; tough but

unconsolidated; grades broadly downward

into:

Bed 12	Sand: medium to fine grained and well to            17.0            143.0

moderately well sorted, some coarse sand in

the upper part of the Bed; marly and clayey

in the upper part with clay content

diminishing in the section; calcareous and

micro- and macrofossiliferous with scattered

shell fragments; slightly glauconitic in the

upper part with glauconite content

diminishing to nil in the lower part; appears

massive and structureless on a small scale,

extremely rudely bedded with mostly gradual

lithologic change down-section;

unconsolidated; olive gray in color; grades

broadly downward into:

Bed 13	Sand: medium grained and well sorted;                 8.0            160.0

slightly argillaceous, slightly calcareous and

slightly fossiliferous; massive and

structureless; unconsolidated and poorly

coherent and competent; grades downward

into:

Bed 14	Silt: very finely sandy, argillaceous,                       1.0            168.0

calcareous and fossiliferous; structureless;

unconsolidated but tough; grades downward

into:

Bed 15	Sand: similar to bed 13, medium grained and        3.0            169.0

well sorted; very slightly argillaceous,

calcareous and fossiliferous; structureless;

unconsolidated and almost clean; the lower

contact is abrupt but not obviously 
		disconformable:

MIDDLE EOCENE, CLAIBORNIAN

OCONEE GROUP

HUBER FORMATION – 23 feet+

Still Branch - equivalent?

Bed 16	Kaolin: finely sandy, no other lithic                       1.0            172.0

components noted; massive, structureless,

plastic and competent; grades abruptly

downward into:

Bed 17	Sand: fine to medium grained and well sorted;      1.0            173.0

argillaceous, no other lithic components noted;

structureless; somewhat consolidated, tough,

hard and brittle; white in color; grades

downward into:

Bed 18	Kaolin: finely sandy, no other lithic                       3.0            174.0

components noted; massive and structureless;

soft, plastic and competent; grades downward

into:

Bed 19	Sand: similar to Bed 7-fine to medium grained      3.0            177.0

and well sorted; argillaceous with some dark,

organic-like stain; massive and structureless;

somewhat consolidated tough, hard, and

brittle; white in color; grades downward into:

Bed 20	Kaolin: no other lithic components noted;              1.0            180.0

structureless, brittle and slickensided; grades

downward into:

Bed 21	Kaolin: silty to finely sandy, the quartz sand         9.25           181.0

content decreases downward leaving almost

pure kaolin at the base (a coarsening upward

sequence); massive and structureless; brittle

and tough; abruptly overlies:

Bed 22	Silty clay to very kaolinitic fine sand: darker,      4.75           190.25

more plastic clay at roughly 191 feet to 192 feet;

no other lithic components noted; mostly

massive and structureless; unconsolidated;

overlies core gap:

MIDDLE EOCENE, CLAIBORNIAN

CLAIBORNE GROUP

CONGAREE FORMATION?

CORE GAP 	The difficulty in recovering core in the updip,      90.0            195.0

nearshore location of the Congaree and Still

Branch Formations is characteristic of the

formations from the Chattahoochee River to

the Savannah River.  The poor core recovery

in sediments in this stratigraphic position,

(lower Lisbon/Still Branch through

“Tallahatta”/Congaree) is due to the

prevalence of well washed and well sorted,

medium to coarse grained sand that is

only slightly argillaceous.  That is, the

well washed sands lack sufficient binding

matrix to hold the quartz sands together;

thus, little to no core recovery.  If this

stratigraphic interval is indeed Congaree

Formation, then an Oconee Group lithology

is not present in that formation in the

vicinity of Clinchfield.

UPPER PALEOCENE, SABINIAN

TUSCAHOMA FORMATION – 13 feet+

Bed 23	Clay: very slightly silty, variably lignitic with         9.5            285.0

lignitic material mostly confined to horizons

or layers, some scattered pyrite noted; thinly

stratified; unconsolidated but competent;

varying shades of olive gray in color; grades

downward into:

Bed 24	Clay: micaceous, carbonaceous and lignitic;          3.5            294.5

thinly stratified; unconsolidated but tough;

dark gray to black in color; grades abruptly

downward into:

UPPER PALEOCENE, SABINIAN

NANAFALIA FORMATION – 2.0 feet

Bed 25	Sand: fine to medium grained and well sorted;      2.0            298.0

argillaceous with a thin layer of clay at the

base, micaceous, lignitic and sooty with some

lignitized wood; mostly massive and

structureless; unconsolidated but competent;

abruptly and probably disconformably

overlies:

LOWER PALEOCENE, MIDWAYAN, DANIAN

CLAYTON FORMATION – 45 feet+

Bed 26	Sand: very coarse grained to fine gravel;                0.5            300.0

structureless; unconsolidated; grades quickly

downward into:

Bed 27	Clay: bioturbated gray clay with, bleached, fine     7.5            300.5

to medium grained sand, slightly micaceous

and sulphurous; unconsolidated and mostly

competent; grades abruptly downward into:

Bed 28	Clay: slightly silty to very finely sandy and          10.0            308.0

sulphurous, the silt/sand component

appears very light in color (bleached as in

the overlying bed); strongly bioturbated but

not completely homogenized; unconsolidated

but very tough and hackly; light gray in color;

grades downward into:

Bed 29	Clay: very slightly silty to very finely sandy            5.0            318.0

and sulphurous; massive and structureless,

well homogenized; unconsolidated, tough and

competent; gray in color; grades abruptly

downward into:

Bed 30	Clay: lignitic and micaceous; structureless            0.5            323.0

except for alignment of lignitic fragments; hard

and brittle; light gray in color; grades abruptly

downward into:

Bed 31	Clay: very similar to Bed 29; grades downward      1.5            323.5

into:

Bed 32	Clay: sulphurous, minor pyrite, possibly some      3.0            325.0

small, detrital, olive colored clay intraclasts;

massive bedded; very tough and competent;

mostly gray in color with mottles of dark olive

gray coloration; grades downward into:

Bed 33	Clay: pyritic and sulphurous with scattered         12.0            328.0

lignitic material, slightly glauconitic at the

base of the Bed; massive and structureless;

very tough and competent, almost hard; dark

gray to mostly black in color; very

gradationally overlies:

Bed 34	Argillaceous “limonite”: some glauconite and         2.5            340.0

mica, one sharks tooth noted; massive

bedded; hard, brittle, fractured and resistant;

abruptly overlies:

Bed 35	Clay: slightly glauconitic, sulphurous and             2.1            342.5

with some limonite; massive and

structureless; unconsolidated but tough;

black in color; abruptly overlies:

Bed 36	Sand: medium to coarse grained and                     0.4            344.6

moderately sorted; glauconitic, sulphurous

and probably a trace of clay minerals although

none were noted; appears to be massive and

structureless; unconsolidated; black in color;

bottom of the core at 345 feet.

________________________________                                      TOTAL DEPTH OF CORE – 345.0 FEET