Paul Huddlestun                                                                                                     Logged ca. 1977

Finished logging – 11/13-16/12                                                                             Finished writing up – 12/12/12

THOMAS 5, GGS-3207, U. S. GYPSUM 76-9

THOMAS COUNTY, GEORGIA

Between Coolidge and Pavo, 3½ miles east of Coolidge

Patten 7½’ Quadrangle

Latitude		N 30° 59.400’                 Elev.  238 Feet Longitude		W 83° 48.555’

Lithostratigraphic

Unit and bed number                 Description                     Thickness        Depth ____________________________________________________________(Feet)_______(feet)_

NO CORE                                                                                 84.0              0.0                                                                                                                          LOWER MIOCENE, AQUITANIAN

CHATTAHOOCHEE FORMATION – 67 feet(

Bed 1		Sand: very fine grained and well sorted; a               8.0             84.0

sporadic trace of very fine mica, slightly

argillaceous with clay gradually and irregularly

increasing down-section, a few laminae of

fullers earth clay, scattered intraclasts

variably dolomitic from nil to a few, thin,

dense, dolostone layers; and minor,

scattered dark minerals; mostly massive

and structureless with the above exceptions;

unconsolidated except for the thin dolostone

layers; variably coherent and competent

(~57% core recovery); the color of the sand

is close to very pale orange (10YR 8/2) and

the clay is close to yellowish gray (5Y 8/1);

abruptly overlies core gap:

CORE GAP	                                                                              4.0             88.0

Bed 2		Interlayered sand, claystone and dolomite:             5.0             92.0

a thin, indurated layer of what appears to

be white (N 9) claystone occurs at the top

of the Bed; overlying a thin layer of

yellowish gray (5Y 8/1), argillaceous, fine

grained, quartz sand; overlying a thin layer

of pinkish gray (5YR 8/1), hard, dense,

slightly silty dolostone with scattered

dark minerals; and overlying a one foot

layer of yellowish gray (5Y 8/1), very

fine grained, well sorted sand with

fullers earth clasts and interstial fullers

earth clay which content increases

downward; overlying a <1 foot layer of

yellowish gray (5Y 8/1), very dolomitic

clay/clayey dolostone; overlying ~1.5

feet of yellowish gray (5Y 8/1) and white

(N 9), intraclastic, argillaceous (fullers

earth), fine grained sand; overlying a

thin layer of argillaceous, intraclastic,

finely sandy dolostone; overlying a thin

layer of yellowish gray (5Y 8/1),

intraclastic, argillaceous (fullers earth),

fine grained sand; variably consolidated

but competent with 100% core recovery;

grades downward into:

Bed 3		Dolostone/very fine sand/fullers earth:                  7.5             97.0

(probably a storm deposit) variably and

irregularly stratified, appears to be very

disrupted sedimentation – difficult to

describe on a small scale; lithic

components variably mixed, mostly

intraclastic to some extent with much

intraclastic dolostone; nonfossiliferous,

wad (MnO2) dendrites occur on the

dolostone layers, other micro-black specks

of uncertain origin and composition;

dolostone layers mostly indurated and

dense, sand and clay unconsolidated but

coherent, dolomitic sand and clay variably

resistant, all competent (100% core

recovery); colors are mostly variegated

and not blended, these include very pale

orange (10YR 8/2) and yellowish gray

(5Y 8/1)

Bed 4		Dolostone: finely sandy with scattered                 10.0            104.5

mollusk molds; massive and structureless;

indurated and competent; colors variable –

range from include very pale orange

(10YR 8/2) to pale yellowish brown

(10YR 6/2) to pinkish gray (5YR 8/1);

grades downward into:

Bed 5		Dolostone: very finely sandy, argillaceous              3.5            114.5

and nonfossiliferous; massive and

structureless; indurated and competent;

very pale orange (10YR 8/2) in color;

grades very broadly downward into:

Bed 6		Dolostone: argillaceous (fullers earth),                   5.0            118.0

variably minor to nil fine quartz sand;

mostly massive and structureless, minor

rude layering based on induration in the

upper part; mostly recrystallized and

moderately consolidated with some more

induration in the upper part, competent;

very pale orange to pale yellowish brown

(10YR 8/2 – 10YR 6/2) in color; grades

abruptly downward into:

Bed 7		Dolostone: somewhat argillaceous with a               1.5            123.0

trace of fine sand and sandy intraclasts in

the upper few inches; massive bedded;

indurated and competent; very pale orange

(10YR 8/2) in color:

Bed 8 	Sand: very fine grained and well sorted;                 5.0            124.5

argillaceous, more argillaceous with clay

clasts in the lower 1 foot; massive and

structureless; unconsolidated but

coherent and competent; light yellowish

gray (5YR 9/1) in color; abruptly overlies:

Bed 9		Limestone: with limestone intraclasts                    4.5            129.5

(appears brecciated in the lower part) and

very irregular inclusions of chert, slightly

argillaceous, appears to have been

granular before recrystallization, irregular

distribution of lithic components and a lot

of variable sized pores or voids that have

the appearance of fossil molds; massive

and structureless; mostly indurated and

competent; the color of the limestone is

close to very pale orange (10YR 8/2), chert

color ranges from medium light gray (N 6)

to light olive gray (5YR 5/2); grades

broadly downward into:

Bed 10	Limestone: mostly a limestone rubble -                  6.0            134.0

all fine grained, matrix-type lithology, some

chert rubble; brittle with irregular fracture;

~35% core recovery for the cored interval;

overlies core gap:

CORE GAP                                                                             11.0            140.0

LOWER OLIGOCENE, VICKSBURGIAN

SUWANNEE LIMESTONE – 105 feet±

The Chattahoochee/Suwannee contact is ambiguous in this core due to poor recovery in the interval.  The criteria employed here to   differentiate between the two formations is: the first occurrence of conspicuous and definite fossils, the occurrence of greenish gray (5GY 6/1) clay in voids or vugs within the Suwannee Limestone and the last occurrence of chert.  The contact can be as high as 138 feet or as low as 151 feet.

Bed 11	Limestone: not much better than overlying            2.0            151.0

material – mostly rubble; dense and chalky

with some fossils and clumps of greenish

gray (5GY 6/1) clay; ~13% core recovery for

the cored interval; overlies core gap:

CORE GAP                                                                             13.0            153.0

Bed 12	Limestone: irregularly and finely granular             9.0            166.0

with varying but considerable amounts of

lime-paste/matrix, a couple of very moldic.

subcoquinoid, fossil bivalve intervals, a

Kuphus incrassatus tube near the top of the

Bed, scattered pods of greenish gray

(5GY 6/1) clay that are probably void or

vug filling formed during the Late

Oligocene subaerial exposure or

nondepositional interval; mostly massive

and structureless except for fossil

concentrations; mostly consolidated or

moderately indurated except for interval of

core gap (the bottom of the run consists of

6 inches of limestone rubble, ~60% core

recovery for the cored interval; the color of

the limestone varies around white (N 9)

and orangish white (10YR 10/2); overlies

core gap:

CORE GAP                                                                               6.0            175.0

Bed 13	Limestone: finely granular with considerable       15.0            181.0

but varying amounts of lime-paste/matrix

and a little chalky; the granular particles

are small, of biogenic origin and nondescript

with a few, small, platy calcitic fragments;

becoming a little more evenly granular down-

section; some scattered mollusk molds and a

couple of concentrations of mollusk molds

similar to the overlying bed - a few of the

molds are relatively large (˃1 inch across)

but mostly non-macrofossiliferous, a few

burrows noted; massive and structureless

except for the fossil concentrations;

consolidated, cemented and competent;

color ranges around very light orange

(10YR 9/2) to very pale orange (10YR 8/2)

with some coloration close to white (N 9);

grades downward fairly abruptly into:

Bed 14	Limestone: mostly very finely granular with           5.5            196.0

many moderately large, exquisitely preserved,

bivalve and gastropods molds and

impressions scattered throughout, these

include the bivalves Glycymeris sp., lucinid

bivalves and the gastropod cf. Ortholax;

massive and structureless; recrystallized,

hard and dense but moderately poor

recovery in coring (40% core recovery –

6 inches of rubble at the base of the run);

white (N 9) to orangish white (10YR 10/2)

in color with some very pale orange

(10YR 8/2) stain; overlies core gap:

CORE GAP                                                                               9.5            201.5

Bed 15	Limestone: similar to Bed 13 except the               14.0            211.0

mollusk molds are more uniformly scattered;

burrows and rhodoliths are scattered

between 311 feet and 315 feet, Dictyoconus

was noted at 218 feet and echinoids

(Rhyncholampus?) was noted at 224 feet;

massive and structureless; consolidated,

well cemented and mostly competent

(~93% core recovery); very light orange

(10YR 9/2) to very pale orange (10YR 8/2)

in color; overlies core gap:

CORE GAP                                                                               1.0            225.0

Bed 16	Limestone: granular with variably abundant        18.5            226.0

lime paste/matrix cement with a few well

washed pelletal/granular places; irregularly

distributed mollusk molds and irregular

distribution of lithic elements (compaction

or storm deposit?); massive bedded;

indurated, chalky and mostly competent

(~97% core recovery); the color of the

limestone is mostly around very light orange

to very pale orange (10YR 9/2 – 8/2) with

more very pale orange (10YR 8/2) in the

lower part; abruptly overlies:

Bed 17	Limestone: fine to medium/coarse textured,          3.5            244.5 		pelletal/miliolid/granular limestone; poorly

sorted calcarenitic sediment; small, medium 						to coarse grain size algae comprises many of

the pellets, miliolids and common

Dictyoconus are all small and identifiable

only under magnification; massive and

structureless; consolidated, uniformly

friable and abrasive and poorly competent

(~30% core recovery in the cored intervals;

pale orange to very pale orange (10YR 7/2 –

10YR 8/2) in color; overlies core gap:

CORE GAP                                                                               8.0            248.0

LOWER OLIGOCENE, VICKSBURGIAN

BRIDGEBORO LIMESTONE – 80 feet

Bed 18	Limestone: (pelletal/algal) coarsely bioclastic,        4.5            256.0

rhodolith-rich; much nondescript, biogenic

debris; abundant, small, pustulose

Lepidocyclina; irregular, chaotic size

distribution of the lithic components;

massive bedded; mostly poor recovery due

probably to hard rhodoliths comminuting

softer inter-rhodolith matrix during coring

(~22% core recovery), the average core

recovery in the formation is almost 10%;

yellowish gray to dark yellowish gray

(5Y 7/2 – 6/2) with some light yellowish

gray (5Y 8/2) color); overlies core gap:

CORE GAP                                                                             15.5            260.5

Bed 19	Limestone: <1 foot of rhodolith debris                   0.75           276.0

recovered; overlies core gap:

CORE GAP                                                                          14.25           276.75

Bed 20	Limestone: ~6 inches of rhodolith debris               0.5            291.0

recovered; overlies core gap:

CORE GAP                                                                             14.5            291.5

Bed 21	Limestone: rhodoliths, limestone chips and           2.0            306.0

Lepidocyclina recovered; overlies core gap:

CORE GAP                                                                             13.0            308.0

NO CORE RECOVERY                                                            15.0            321.0

UPPER EOCENE, UPPER JACKSONIAN

OCALA GROUP

CRYSTAL RIVER LIMESTONE – 365 feet

Bed 22	Limestone: the size range of the bioclastic,          15.0            336.0

calcarenitic material is considerably less

than that of overlying limestone beds or

formations; irregular distribution of lime-

paste cement, some intervals thoroughly

cemented and nondescript but with some

small fossil molds, lime-paste/matrix

content decreases down-section; large

Lepidocyclina are present throughout

and also decrease irregularly in size

down-section, the larger foraminifera

Asterocyclina, Operculinoides and

Heterostegina are present but rare; small

rhodolith algae are locally conspicuous;

massive and structureless; the recovered

core is well cemented, brittle and mostly

competent (~86% core recovery); the color

of the limestone ranges around very light

orange (10YR 9/2 and whitish orange

(10YR 10/2); overlies core gap:

CORE GAP                                                                             10.0            351.0

Bed 23	Limestone: Lepidocyclina coquina, finely               7.0            361.0

calcarenitic; nondescript, angular

biodebris with few larger biodebris

fragments, all well washed; the

Lepidocyclina size is small (on the order

of millimeters), very rare Asterocyclina

and Heterostegina are also noted;

massive bedded and the Lepidocyclina

orientation is mostly chaotic and

random; well cemented and competent;

very light orange (10YR 9/2) in color;

grades very broadly downward over

about 1 foot into:

Bed 24	Limestone: very similar to overlying bed              23.25           368.0

but generally and irregularly coarsening

down-section; more chalky matrix, small

rhodoliths, few bryozoans and other

biodebris; massive bedded; random/chaotic

orientation of the Lepidocyclina; recovered

core is consolidated and well cemented

but the recovery is only poor (~29% core

recovery); very light orange (10YR 9/2) to

very pale orange (10YR 8/2) in color;

More small rhodoliths and more

intragranular paste/matrix below

~376 feet;

Amusium ocalanum noted at ~379 feet;

The basal contact is obscure because of

poor core recovery, appears to abruptly

overlie;

Bed 25	Dolostone: finely sucrosic, dense and               25.75           391.25

porous in the upper part (pores may be

remnants of small fossil molds); becoming

gradually and irregularly more porous and

finely sucrosic down-section; fossil

remnants become identifiable as former

bioclastic hash below ~399 feet and are

conspicuous at ~410 feet; massive and

structureless; recrystallized, indurated

and mostly competent (~89% core recovery),

the broken core surface is abrasive to the

touch; mostly pale yellowish brown

(10YR 6/2) in color, closer to pale orange

(10YR 7/2) in the lower part; fairly abruptly

grades downward into:

Bed 26	Dolostone: sucrosic, moldic and coquinoid,           6.5            417.0

some Lepidocyclina molds identifiable as

such; massive bedded, platy fossils and

Lepidocyclina molds occur in random

orientation; recrystallized, indurated and

competent; grayish orange (10YR 7/4) to

very pale orange (10YR 8/2) in color;

grades downward into:

Bed 27	Limestone: some rude, thin dolomitic                    9.5            423.5

intervals, probably somewhat and variably

dolomitic throughout; originally was

calcarenitic but is now somewhat sucrosic

and porous; matrix/lime-paste content is

variable; some Lepidocyclina and algae;

mostly massive bedded; recrystallized and

competent; very light orange (10YR 9/2 to

very pale orange 10YR 8/2) in color;

grades downward into:

Bed 28	Dolostone: finely sucrosic, variably moldic             3.5            433.0

(subcoquinoid to almost nil fossils); generally

massive bedded but with some stratification

and irregular structures (depositional/

compaction?); recrystallized and competent;

grayish orange (10YR 7/4) to pale yellowish

brown (10YR 6/2) in color; grades

downward into:

Bed 29	Limestone: recalcified and finely sucrosic,           18.7            436.5

most fossils eliminated by recrystallization

leaving the limestone variably porous, and

slightly dolomitic, content of chalky 	matrix/

lime-paste is considerable but variable;

appears to have been originally a fine to

moderate coquina or subcoquina; massive

and structureless; recrystallized and

competent; very light orange (10YR 9/2 to

very pale orange 10YR 8/2) in color; grades

downward into:

Bed 30	Dolostone: sucrosic, variably moldic and               6.8            455.2

porous; fossils mostly gone but still

recognizable as such; massive and

structureless; recrystallized and competent;

grayish orange to pale orange (10YR 7/4 –

10YR 7/2) in color; grades downward into:

Bed 31	Dolomitic limestone: similar to overlying

bed; but dominantly calcareous grading                3.0            462.0

downward into limestone; recrystallized,

indurated and competent; pale orange

(10YR 7/2); grades downward into:

Bed 32	Limestone: recalcified and sucrosic,                     10.0            465.0

generally fine to medium and even

textured; probably slightly and variably

dolomitic with some thin dolostone

intervals; some fossils still evident but

most fossils are gone; massive and

structureless; recrystallized and

competent; mostly very light orange

(10YR 9/2) in color; grades downward

into:

Bed 33	Limestone: variably recalcified and sucrosic        22.0            475.0

and the sucrosity varies from fine to coarse

texture, variably porous; fine grained,

chalky matrix dominant throughout the

Bed, probably slightly dolomitic to some

degree throughout the Bed (probably more

so in the upper part and less dolomitic

down-section); variably fossiliferous with

coarser textured intervals being

nonfossiliferous, fossil preservation

gradually improves down-section (bivalve

molds noted at 481 feet); small, thin

Lepidocyclina become noticeable in cross-

section on the core surface in the upper

part, becoming conspicuous and unaltered

down-section; mostly massive 	and

structureless but with some rude

dolostone layers; recrystallized and

competent; the color ranges around

orangish white (10YR 10/2) to very pale

orange 10YR 8/2) with some light grayish

orange (10YR 8/4), almost white (N 9) in

a few places;

Dolostone layers occur at 481 feet to

483 feet, 487 feet to 489.5 feet and

495.5 feet to 497 feet;

An echinoid noted at ~487 feet;

Lepidocyclina abundant below 498 feet,

originally a Lepidocyclina limestone;

Grades downward into:

Bed 34	Limestone: generally calcarenitic and                  47.0            497.0

fossiliferous with Lepidocyclina but mostly

recalcified and finely granular with variable

and minor sucrosity, probably slightly

dolomitic in places, not well washed –

matrix/lime-paste appears to be the

dominant lithic component; a few coarsely

fossiliferous, bio-rubbly intervals; some

large Lepidocyclina but mostly small,

delicate ones; mostly massive bedded but

some faint suggestions of layering here and

there, the Lepidocyclina generally are in

roughly horizontal orientation but not

invariably; mostly recrystallized,

consolidated, compact and competent;

mostly around orangish white

(10YR 10/2) to very pale orange

10YR 8/2) in color; grades very broadly

downward into:

Bed 35	Limestone: generally becoming more visibly         45.0            544.0

bioclastic and angular, more calcarenitic

and less matrix/lime-paste – the matrix is

still the dominant lithic component but very

gradually decreases down-section whereas

the fossil diversity gradually increases

down-section along with more calcitic

shells and shell fragments (pectenids and

Amusium); Lepidocyclina is common and

the surface of the core is very abrasive;

there is still a sucrosic interval between

548 feet and 549.5 feet and the first

selenite is noted at ~580 feet; mostly

massive and structureless; slightly

recrystallized at intervals, consolidated

and mostly competent (~89% core recovery);

the color ranges around orangish white

(10YR 10/2) to very pale orange (10YR 8/2);

grades downward into:

Bed 36	Limestone: similar to the overlying bed                 7 .0            589.0

but matrix/lime-paste content increases

again, the limestone is slightly sucrosic,

there are minor scattered occurrences of

selenite and fewer fossils - the fossils

present are more poorly preserved; the

Bed is somewhat more calcarenitic with

improved fossil preservation in the lower

part but the preservation goes to hell in

the lower few inches; massive and

structureless; recrystallized, indurated

and competent; white (N 9) to very light

orangish white (10YR ˃10/2) in color;

grades downward into:

Bed 37	Calcareous selenite and selenite: sucrosic             3.5            596.0

limestone with intragranular selenite in

optical continuity in the upper part;

grading downward into more selenitic

lithology with some Lepidocyclina, an

echinoid and shell fragments in the

middle part, grading downward into

selenite with little calcite and perhaps

some dolomite; massive and structureless;

recrystallized, dense and competent;

yellowish gray (5Y 8/1) in color; basal

contact irregular, grades downward over

inches to ˃1 foot into:

Bed 38	Limestone: broadly similar to Bed 36 but             16.5            599.5

more matrix/lime-paste; the same moderate

diversity dominated by Lepidocyclina with a

greater tendency toward horizontal

orientation, some pectenids and Amusium,

rare bryozoans and small rhodoliths; mostly

massive and structureless but some very

crude stratification at intervals; indurated,

recrystallized, less abrasive than overlying

bed and competent; very light orange

(10YR 9/2) to very pale orange 10YR 8/2) in

color; very broadly gradational from 610 feet

to 616 feet into:

Bed 39	Limestone: bioclastic/calcarenitic with                44.5            616.0

angular biodebris particles and fragments,

and matrix/lime-paste; few Lepidocyclina

and scattered and rare Operculinoides and

Asterocyclina; not well mixed lithic

assemblage; a higher diversity than

overlying beds – containing rare corals,

bryozoans, small rhodoliths, etc.; massive

bedded but has a mega curdled appearance

due to poor mixing of the fairly well washed

biodebris and the influx of matrix/lime-

paste (storm disturbance, differential

compaction or simply a result of a

1-dimensional view of disturbed bedding?);

consolidated and competent; the color

ranges around orangish white (10YR 10/2)

to very pale orange (10YR 8/2);

Asterocyclina and a crab claw noted at

~628 feet;

Operculinoides noted at 635 feet, 643 feet,

645 feet and 658 feet;

Asterocyclina noted at 643 feet, 650 feet

and 659.5 feet;

Grades downward into:

Bed 40	Limestone: similar to above except selenite            7.5            660.5

is more common but minor and scattered,

some selenite vugs; Lepidocyclina and

Asterocyclina still present; massive and

structureless; consolidated and competent;

orangish white (10YR 10/2); grades

downward very broadly and subtly into:

Bed 41	Limestone: similar to overlying bed but better      22.0            668.0

homogenized in terms of size-distribution,

still incompletely mixed and where less

matrix is present, the limestone can be seen

to have been a calcarenitic, bioclastic

hash; scattered concentrations of selenite;

more general fine textured matrix, lower bio-

diversity, more Lepidocyclina in scattered

concentrations and some well preserved

mollusk impressions; mostly massive and

structureless and some crude hints at

stratification, Lepidocyclina displays a

tendency toward horizontal orientation;

mostly dense, very indurated and competent,

probably recalcified; the color varies around

orangish white (10YR 10/2) and very pale

orange (10YR 8/2);

Selenite in optical continuity within the

limestone noted around 675 feet to

678 feet;

Spondylus noted at 683 feet, Amusium

noted at 685 feet and a small, well

preserved, Cassis (gastropod helmet shell)

noted at 687 feet;

Grades downward into:

Bed 42	Limestone: as above slightly dolomitic,                11.0            690.0

more chalky with matrix/lime-paste,

some very fine sucrosity in places and

transparent, mica-like selenite at 695 feet;

in addition to Lepidocyclina, Heterostegina

was noted at ~700 feet, few if any

Nummulites that are characteristic of the

underlying formation were noted; massive

and structureless; indurated and

competent; the color ranges around very

light orange (10YR 9/2) and very pale

orange (10YR 8/2); grades abruptly

downward into:

UPPER EOCENE, LOWER JACKSONIAN

OCALA GROUP

WILLISTON LIMESTONE – 89 feet

Bed 43	Dolostone: very selenitic with nodular gypsum      3.4            701.0

(the first occurrence of milky, nodular

gypsum is at 701 feet); fossiliferous with

the first definite occurrence of Nummulites;

massive bedded; recrystallized, indurated and

competent; the color in the upper part ranges

from very pale orange to pale yellowish brown

(10YR 8/2 – 10YR 6/2) whereas in the lower

part it is closer to pale orange to pinkish gray

(5YR 7/2 – 5YR 8/1); grades downward into:

Bed 44	Limestone: dolomitic and/or finely selenitic,        18.1            704.4

some minor scattered intragranular selenite

crystals and some scattered gypsum nodules

large and small (millimeters to ˃1 foot) with

embayed margins; fossiliferous with mostly

Nummulites and thick and thin

Lepidocyclina in a very finely crystalline

matrix (some megalosphaeric Lepidocyclina

noted), some concentrations of larger

foraminifera; some rare mollusk molds or

calcitic mollusk fragments; massive and

mostly structureless, the orientation of

Lepidocyclina and Nummulites are scattered

randomly in some intervals and with a

tendency toward horizontal in other

intervals; recrystallized (except for larger

foraminifera?), dense, indurated and

mostly competent (~89% core recovery);

the color ranges around very light orange

(10YR 9/2) and very pale orange (10YR 8/2);

Spondylus noted at 705 feet, Nummulites

are frequent around 707 feet and

Operculinoides noted at 708 feet;

Grades downward into:

Bed 45	Calcareous dolostone/dolomitic limestone:            2.5            722.5

sucrosic with scattered gypsum nodules;

white, chalky Lepidocyclina and Nummulites;

massive and structureless; recrystallized

and competent; pale yellowish brown

(10YR 6/2) to light brownish gray

(5YR 6/1) in color; grades downward

into:

Bed 46	Limestone: similar to overlying bed except             4.5            725.0

it is less dolomitic and Lepidocyclina and

Nummulites become less conspicuous in

the lower part of the Bed. massive and

structureless; recrystallized and competent;

pinkish gray (5YR 8/1) in color; abruptly

overlies:

Bed 47	Gypsum: massive, structureless gypsum               1.5            729.5

nodule; competent; light gray to very light

gray (N 7 – N 8) in color; abruptly overlies:

Bed 48	Limestone: chalky, somewhat dolomitic                 4.5            731.0

and sucrosic – has the appearance of a

lime mud; rare gypsum nodules; larger

foraminifera less common and

conspicuous; massive and structureless;

recrystallized and competent; very pale

orange (10YR 8/2) in color; grades

downward into:

Bed 49	Limestone: dolomitic, very finely sucrosic,           15.0            735.5

very fine textured, chalky and nondescript

lithology; a thin zone of gypsum nodules is

present from 742 feet to 743.5 feet, some

of the nodules having merged together to

form one nodule; Nummulites are frequent

to common in occurrence (larger ones in

the lower part), Lepidocyclina also is

present; an echinoid was noted at 748

feet; mostly massive and structureless

except for the interval of nodules;

recrystallized, indurated and competent;

the color ranges around very light orange

(10YR 9/2) and very pale orange

(10YR 8/2) with some pale orange

(10YR 7/2); grades downward into:

Bed 50	Limestone: less dolomitic than overlying                6.5            750.5

bed but with more scattered gypsum

nodules; few larger foraminifera but an

echinoid noted at 754 feet; otherwise the

lithology is similar to the overlying bed;

finely sucrosic, fine textured, chalky and

lithologically nondescript; massive and

structureless; recrystallized, indurated

and competent; the color ranges around

very light orange (10YR 9/2) to very pale

orange (10YR 8/2); grades abruptly

downward into:

Bed 51	Dolostone: sucrosic and fossiliferous with             5.0            757.0

common white Nummulites and rare

Lepidocyclina, all larger foraminifera gone

where dolomitization is the most extreme,

all larger foraminifera are chalky;

abundant large and small gypsum

nodules; massive and structureless;

recrystallized, indurated and competent;

pale orange (10YR 7/2) to grayish orange

(10YR 7/4) in color; grades downward

into:

Bed 52	Limestone: dolomitic, finely sucrosic and               2.5            762.0

fossiliferous with Nummulites and

Lepidocyclina; massive and structureless;

recrystallized, indurated and competent;

pale orange (10YR 7/2) in color; grades

downward into:

Bed 53	Limestone: finely granular and slightly                24.0            764.5

chalky but not sucrosic, slightly dolomitic

with a trace of selenite and a couple of

“bands” of gypsum nodules; the limestone

has the appearance of indurated lime-

mud with scattered small fossils and

Nummulites, few Lepidocyclina and rare

Operculinoides, fossils and larger

foraminifera becoming sparse below

about 769 feet; massive and structureless

except for the “bands” of gypsum nodules;

indurated and competent; coloring

slightly variable around pale orange

(10YR 7/2) to pinkish gray (5YR 8/1),

very light orange to very pale orange

(10YR 9/2 – 8/2) and pale orange

(10YR 7/2);

Although uncommon, Lepidocyclina are

more conspicuous relative to Nummulites

again between ~775 feet and ~782 feet;

Less dolomitic below ~784 feet;

Fossils and larger foraminifera almost

absent below ~787 feet; the limestone

consists only of an indurated lime mud;

Abruptly and irregularly overlies:

Bed 54	Gypsum: massive gypsum nodule with                  2.0            788.5

inclusions of unabsorbed limestone;

massive and structureless with very

irregular upper and lower surfaces;

competent; light gray to very light gray

(N 7 – N 8) in color; abruptly and

irregularly overlies:

MIDDLE EOCENE, UPPER CLAIBORNIAN

UNNAMED CLAIBORNIAN LIMESTONE – 416 feet(

Interval 1 – 169 feet

Gosport-equivalent?

Bed 55	Limestone: chalky, finely and irregularly             148.0           790.5

equigranular, granular material is

moderately well sorted and of bioclastic

origin; sparse small fossils and platy, calcitic

fossil debris in random orientation; scattered

and variable concentrations of larger

foraminifera, from abundant to nil; scattered

intervals of partial dolomitization, milky

gypsum nodules occur below the upper part

of the Bed; mostly massive and structureless

except for scattered bioturbated intervals;

partially recrystallized, well cemented and

competent, more compact and less porous

than the overlying Ocala Group; color of

most of the limestone is orangish white

(10YR 9/2), dolomitized limestone is very

pale orange (10YR 8/2);

Rare to frequent, small delicate

Lepidocyclina scattered throughout granular

calcarenite, rare scattered burrows, very

rare Nummulites at ~812 feet;

Appears bioturbated and somewhat

dolomitic between 817.5 and 821 feet;

Rare larger foraminifera at ~823 feet;

More larger foraminifera and increase in

numbers of Nummulites below ~825 feet;

A concentration of larger foraminifera at

~833 feet, especially Nummulites, also some

platy, calcitic fossil fragments; concentrations

of larger foraminifera in this part of Bed 55

are quite variable – ranging from rare to

common at intervals but are mainly scattered

or sprinkled throughout; the basic lithology

is much the same but with more nondescript

pelletal and bioclastic material and echinoid

fragments;

Thick margined sand dollars? at 839.542 feet;

Top of milky, gypsum nodules at 845 feet,

concentration of gypsum nodules is irregular

but increases with depth;

Appears bioturbated and burrowed at ~848

feet;

Abundant Nummulites at ~860 feet and

discontinuously abundant down-section, some

“discocyclinids”?

Texture of limestone becomes conspicuously

finer with more micrite and fine pelletal

calcarenite below ~876 feet, larger

foraminifera are fewer and less conspicuous;

The limestone is distinctly finer textured and

sucrosic calcite becomes evident below 882

feet, still appears to be mainly fine grained

bioclastic debris with micritic or calcilutitic

matrix, core surface is smoother but still gritty

to the touch, larger foraminifera rare with

scattered delicate Nummulites and

“discocyclinids”?

Small concentration of larger foraminifera at

~890 feet;

Top of chert nodules at ~912 feet, light gray

(N 7) in color, concentrations of chert nodules

increase down-section;

Limestone core is vertically fragmented and

broken between ~913 and ~916 feet;

Four inches of thinly layered limestone “biscuits”

at ~918 feet;

Chert concretion at ~920 feet, light gray (N 7)

in color;

Chert and gypsum concretions at ~924 feet;

Chert filled burrows at ~925 feet;

Slightly dolomitic with scattered dolomite

rhombs between ~931 and 935 feet;

Very finely granular limestone with rare larger

foraminifera, scattered chert concretions, and

some milky gypsum nodules below ~934 feet;

Irregular shaped chert and gypsum nodules

together, both closely related spatially, gypsum

encloses and embays irregular clasts of

limestone from ~934 to 937 feet;

Limestone gradually becoming more

dolomitic below ~935.5 feet (sucrosic at

~937 feet – moderately slow HCl reaction),

grading downward into pure, finely

sucrosic dolostone at ~938.5 feet;

Bed 56	Dolostone: gypsiferous, chert and milky              20.5            938.5

gypsum nodules, selenite occurs in optical

continuity or as intra-matrix throughout

the bed; very fine grained and sucrosic

(glitters in the sun light); massive and

structureless; indurated, hard, and very

competent; colors are complexly mottled

and range from grayish orange – pale

grayish orange (10YR 7/4 – 10YR 8/4) to

very pale brown (10YR 6/2);

Abundant gypsum nodules and selenite in

optical continuity within dolostone matrix

around 940 feet;

Chert nodule at ~941 feet and nodules

increase sporadically in number down

section;

Dolostone is completely recrystallized below

~942 feet;

Chert nodules are irregular shaped and

rounded, like some sort of burrow filling

from ~950 to 957 feet – chert colors range from

light olive gray (5Y 6/1) to pinkish gray

(5YR 8/1);

Gypsum and chert nodules occur together

at ~953 feet – gypsum appears to embay

matrix, chert has appearance of burrow-fill;

Grades downward over about two feet into:

Interval 2 – 247 feet+

Lisbon/Blue Bluff/Cook Mountain equivalent?

Bed 57	Limestone: variably and very finely                    146.5            959.0

equigranular; slightly dolomitic (glitters in

the sunlight), scattered occurrences of

chert concretions and chert layers (less

than 1 foot thick), a possible scattered

trace of clay minerals; only larger

foraminifera have been noted and they are

rare and scattered; except at the top of

Bed 57, larger foraminifera include rare

Nummulites (with 10 to 15 chambers per

whorl) but they occur in some frequency at

some levels, some primitive Operculinoides

(20 chambers per whorl), “discocyclinids”

begin to appear farther down the section

and vary in abundance from frequent to nil,

Lepidocyclina is exceedingly rare but mostly

absent, only a trace of macrofossils but

they are mostly absent; gypsum nodules

and selenite are absent;

Mostly massive and structureless except

where larger foraminifera define some

bedding planes, vague indication of bedding

and rare bioturbation elsewhere;

Well cemented and somewhat variably

competent, the average core recovery is

~81% but varies in core runs from 100%

to ~23%, most of the Bed is competent;

The color of limestone is mostly orangish

white (5Y 9/2) with some very pale orange

(5Y 8/2):

Gypsum nodule at ~964 feet;

A trace of clay and bioturbation at ~965 to

967 feet;

Core fractured at ~968 feet

Nummulites occurs along bedding plane at

~976 feet;

Scattered thin Nummulites and primitive

Operculinoides? at ~985 feet;

Large chert nodule at ~988 to ~988.5 feet,

chert color is very light olive gray to light

olive gray (5Y 7/1 to 5Y 6/1);

Appears slightly more dolomitic below ~989

feet;

Chert filled burrow at ~990 feet;

Thin chert layer at ~992 feet;

Large chert nodule at 992.5 to 993 feet;

Core Gap from ~1006 feet to ~1021 feet;

One foot thick chert layer at ~1021 feet,

chert nodules and thin chert layers are

common below this depth;

One foot of thinly layered limestone at

~1022 feet;

Rare and scattered Nummulites and

Operculinoides on bedding plane at

around 1025 feet;

Fragmented chert at ~1027.5 feet;

Rare and scattered Operculinoides at

~1030 feet;

Dolomite absent or not apparent below

~1033 feet;

Several thin chert layers from ~1033.5 feet

to ~1037 feet;

Rare “discocyclinids” on bedding plane at

~1034 feet;

Core broken and vertically fragmented

between ~1040 feet and ~1043 feet;

Gray (medium light gray to light gray – N 6

to N 7) chert nodules between ~1044 feet

and ~1046 feet;

Slightly dolomitic again from ~1046 feet to

~1048 feet – “discocyclinids”, Operculinoides, and

rare Nummulites define bedding surfaces

around ~1048 feet;

Chert that appears embayed and with small,

druzy quartz crystals at ~1048 feet;

Frequent “discocyclinids”, rare Operculinoides

and a large Lepidocyclina on bedding

surfaces around 1050 feet, color of limestone

darkens to very light orange (10YR 8/2);

Large gray (medium light gray to olive gray –

N 6 to 5Y 4/1) chert nodule at ~1053 feet;

Scattered occurrences of olive gray (5Y 4/1)

chert that are rounded to very irregular in

shape below about 1059 feet, “discocyclinids”

becoming larger and more common, a few

large Lepidocyclina also are present;

Operculinoides becoming a little more

frequent below ~1064 feet;

Limestone becoming more finely granular

below ~1065 feet, granules difficult to

characterize with a hand lens;

Dark olive gray (5Y 3/1) chert at ~1065.5

feet ~1067 feet,

A pectenid mold noted at ~1072 feet;

“Discocyclinids” and Operculinoides

becoming rare below roughly 1073 feet;

Operculinoides decline and are absent

below roughly 1076 feet;

Core is fragmented and broken vertically

around 1080 feet;

Olive gray (5Y 4/1) chert appears to

embay the limestone at ~1083 feet;

One foot of very broadly conchoidal,

calcareous dolostone at ~1084 feet, may

be siliceous;

Thin layers of olive black to olive gray

(5Y 2/1 to 5Y 4/1) chert from ~1095 feet

to ~1101 feet, some scattered Nummulites

in the associated limestone;

Grades downward into:

Bed 58	Dolostone: very finely sucrosic, with chert            3.5           1105.5

nodules and vugs with druse quartz – one

proto-quartz geode with euhedral quartz

crystals at ~1107 feet, calcareous in lower

1 foot; massive and structureless;

recrystallized indurated, dense and

competent; color is closest to pale yellowish

brown (10YR 6/2) but a bit more yellowish;

grades downward into;

Bed 59	Limestone: essentially the same lithology as       97.0           1109.0

Bed 57, very fine textured and progressively

finer textured down-section with more finely

micritic to lutitic matrix, almost a lime mud;

scattered and common gray/olive gray chert

nodules and thin chert layers, maybe some

interstitial silica in lower part, one thin

clayey layer noted and probably a trace of

clay minerals throughout, mostly

unfossiliferous but a few, scattered, thin,

delicate fossils are present on bedding

surfaces (e.g. bryozoans and smaller

foraminifera – “discocyclinids” disappear

below about 1130 feet);

Limestone is mostly layered and flaggy, some

broadly “conchoidal” fractures occurring as

in overlying bed, some scattered, very thin

bedding is present throughout but is

prominent below about 1175 feet, some

bioturbation is present in the lower part of

the Bed;

Indurated, dense and brittle; 	cemented but

variably competent with only moderate

average competence (~57% core recovery),

range of core recovery in different core runs

range from ~15% to 100%;

The color of limestone is mostly very pale

orange (10YR 8/2):

Rare to frequent “discocyclinids” on bedding

surfaces at ~1110 feet to ~1111 feet;

Core gap from 1115.5 feet to ~1126.0 feet

with olive gray (5Y 4/1) chert fragments at

the bottom of the core run;

“Discocyclinids” as well as other larger

foraminifera absent below ~1130 feet;

Chalky, thinly layered and platy (“poker

chips” and “biscuits”), dense and hard, very

finely granular limestone with a few,

scattered, delicate fossils noted at ~1135

feet to ~1135.5 feet;

A few pectenid shells noted at ~1140 feet;

Very thinly layered to laminated,

argillaceous? very finely micritic to lutitic

limestone at about 1166 feet; color ranges

from very pale orange (10YR 8/2) to

orangish white (10YR 9/2) with some

bluish white (5B 9/1);

A few smaller foraminifera noted at around

and below ~1190 feet – Lenticulina in

particular;

Appears bioturbated, siliceous and more

lutitic with some pyrite between ~1192 and

~1194 feet;

Limestone is thinly bedded to laminated

from ~1199 feet to ~1200 feet, limestone

remains very finely granular to T.D.;

Bottom of core at 1206 feet.

___________________________                	           	                                         TOTAL DEPTH – 1206 FEET

3/11/21